## Slide 1: EE 735 (Microelectronics Simulation Lab)
Assignment -3
(23rd August 2023)
TA : Chenna Satya Sai Teja
Ph no: 7076315403
Mail: 22m1132@iitb.ac.in
Instructor: Prof. Saurabh Lodha

## Slide 2: Question 1
P-N junction diode (see Figure 1:(a)). Thickness of the P and N regions is L = 1.5 μm each. For the following doping profiles, plot profiles 1-3 (from introduction section) with and without depletion approximation and plot profiles 4-5(from introduction section) without depletion approximation
  Abrupt junction (see Figure 1:(b)) with dopant concentrations NA = (1+a)1015/cm3 ND = (1+b)1015/cm3.
  Linearly graded junction (see Figure 1:(c)) with bulk dopant concentrations NA = ND = (1+b)1015/cm3

## Slide 3: Question 1 (cont.)
Profiles to be plotted:
Potential (V)
Electric Field(E)
Charge concentration ((where q is electron charge)
Electron (n) and hole (p) concentrations
Energy band diagram depicting conduction band minimum (EC ), Valence band maximum (EV), mid gap energy level (Emid) and Fermi energy level (EF) .
Note: Doping Profile shown is valid in depletion region only

## Slide 4: Depletion Approximation vs Exact Analysis
The approximation has two components that can be stated as follows:
The Carrier concentrations are assumed to negligible compared to the net doping concentration in a region –xp < x < xn.
The charge density outside the depletion region is taken to be identically zero.

## Slide 5: Depletion Approximation vs Exact Analysis (cont.)
With Depletion approximation
Without Depletion approximation

## Slide 6: Solving Poisson Equation
Step 1. Discretize the given device into N nodes
Step 2. Define Dopant profile.

## Slide 7: Solving Poisson Equation
Step 3: On the basis of Poisson’s equation for node i, write the matrix A, V, and B and let F=AV-B
Step 4: Fill the values of matrix V with
with your initial guess.

## Slide 8: Solving Poisson Equation
Step 5: Create Jacobian Matrix (J) and solve using newton Raphson method.
Newton Raphson Method

## Slide 9: Solving Poisson Equation
Step 6: Obtain a solution for ΔV as Δ𝑉=−(You can write “J\f” to obtain in matlab)

## Slide 10: Solving Poisson Equation
Step 7: Obtain new value of Potential profile,
Step 8: Obtain f(V) and J(V) for
Step 9: Follow steps 5 to 8 for sufficiently large number of times or when the difference( is very small
Step 10: Obtain electric field, E

## Slide 11: Solving Poisson Equation
Step 11: Plot Energy band diagram wrt Ef

## Slide 12: Question 2
structure with abrupt junctions. NA = 10^17 /cm3 inside P+ region; whereas ND = 10^17 /cm3 inside N+ region and 10^15 /cm3 inside N region. With the thickness of P+ and N+ regions fixed at 0.5 μm each, vary the thickness of N region over the range (1, 2, 3) μm.
Show the variation of (V vs X) as a function of N region length (LN ). (Plot all the profiles in a single plot)
Discuss your observation. (The profiles asked in the Introduction section should be plotted only for LN = 2μm).

## Slide 13: Question 3

## Slide 14: Boltzmann Approximation
Boltzmann approximation assumes that the Fermi energy is at least 3kT from the band edges.

## Slide 15: Reference
Section 5.1 from “Semiconductor Device Fundamentals” by Robert F Pierret for “Depletion Approximation”.
Section 4.4 from “Advanced Semiconductor Fundamentals” by Robert F Pierret for “Boltzmann Approximations and other formulas used for finding n and p concentrations”

## Slide 16: Thank you..